## Slide 1: Chatterpaul Joseph
Seeker Trade Study - Homework
Notes: https://www.free-power-point-templates.com/free-green-design-powerpoint-template/

## Slide 2: Agenda
Laser & LADAR Link Budget, Trade-offs and Feasibility
Monostatic vs Bi-static RF Seeker
  Surface to Air
COTS Component, Software & Test Tools, Size, Power, Weight & Cost, Calibration

## Slide 3: Laser 101
Focusing
Target
D
Laser Source
F
Peak Power P(kW) | Wavelength λ(um) | Diameter D(cm) | Beam Quality BQ | Focal Length(km)
1 – 10 | ~1 | 5 – 10? | 1.4 – 2 | ≤ 20
Pulse Width (ns) | Pulse Energy (mJ) | Cost ($K) |  | 
.010 – 10 | .01 – 10 |  |  | 
Pulse Width (ns) | Pulse Energy (mJ) | Cost ($K) |  | 
.010 – 10 | .01 – 10 |  |  | 
d
Diffraction Limited Focal Spot on Target
Intensity (W/cm2) is Power on Target over Area
tx is the transmission fraction through air/haze/cloud/etc.
Notes: Vehicle: https://www.defense.gov/observe/photo-gallery/igphoto/2002121156
Lens: https://www.cambridgeincolour.com/tutorials/camera-lenses.htm
UAS Target: https://www.researchgate.net/figure/US-DoD-Unmanned-Aerial-System-Group-Classifications-14_fig3_295873907
*Based on laser cutter: https://www.google.com/search?q=high+power+laser+cutter+cost but it’s not eye-safe

## Slide 4: A Laser Performance Example: Power on Target
Notes: Bigger Aperture (D) Smaller Focus (d)
Effects that degrade Beam Quality (BQ) are thermal distortion in optics, optical quality (coke bottle shape curve), atmospheric turbulence and point jitter blur the spot
Example:
“Hard” Structure Lethality – Direct Energy
“Soft” Lethality – Blinds IR Seekers

## Slide 5: A Laser Performance Example: Detect Target
Using a form of the LADAR/LIDAR range equation to determine the detected off a target
is the target optical cross section (OCS)
The ability to see the reflections off a target is dependant on the optical cross section of the target. If there is an IR seeker at your laser’s wavelength, then there could be a strong reflection like a cat’s eye reflecting light.
A LADAR would need at > ~60 (dBm) for detection, which would requires a Higher Energy, Larger Diameter and Larger OCS
What is reasonable OCS and Power Receiver for an IR camera and delta temperature is need?
Notes: Cat’s Eye: https://www.youtube.com/watch?v=qU6Sz1SIwPs
Example Designator: https://www.military.com/video/operations-and-strategy/air-strikes/laser-targeted-strike-in-afghanistan/2707623470001

## Slide 6: Commercial Off The Self Laser Challenges
- Atmospheric effects can potentially make LADAR detectable to adversaries
- Short pulses mean better range and resolution but also scatter off particulates and water droplets in the atmosphere
- Lasers are inefficient, so higher prime power and heat dissipation issues
Atmospheric Loss and 1/R4 are significant non-design terms in the power receive
Notes: Particle Radius Wavelength: https://www.e-education.psu.edu/meteo300/node/785
Transmitted by the Atmosphere: https://commons.wikimedia.org/wiki/File:Atmospheric_Transmission.png
COTS Rare-earth Lasers: https://www.researchgate.net/figure/Summary-of-upconversion-rare-earth-doped-ZBLAN-fiber-lasers-with-the-highest-output_tbl2_43170278

## Slide 7: RF Rectangular Antenna Phased Array Hardware
Peak Power P(W) | Wavelength λ(mm) | Antenna Gain G (dB)
256*.010 = ~2.5 to 10 | ~10 | 24
Grating Lobes
Chart: 
| 4 | 16 | 64 | 256
ROM K$ | 2 | 8 | 16 | 25.6
# RF Channel
Cost $K
To get 30 (dB) would require 32x32 array
Pulse Width PW(us) | Pulse Repetition Frequency PRF (kHz) | Process Bandwidth BW(MHz)
< ~60 | < ~8 | 1
Pulse Width PW(us) | Pulse Repetition Frequency PRF (kHz) | Process Bandwidth BW(MHz)
< ~60 | < ~8 | 
(> 20 for unambiguous range rate)
Smaller bandwidth, lower noise level but also lower range-resolution
Recommend Design Tools:
CST – Antenna
Microwave office - HW
Python Analysis
Notes: https://www.anokiwave.com/products/index.html
https://www.xilinx.com/products/boards-and-kits/device-family/nav-zynq-ultrascale-plus-rfsoc.html

## Slide 8: Radar Monostatic & Bi-static Link Budget
For reasonable power and gain parameters, the SNR is too low for the given RCS and geometry, resulting in the target being undetectable.
Monostatic Parameters:
  RCS = -20 (dBsm), Bw = 100e3 (Hz)
  Ptx = 10 (W), Freq=30e9 (Hz)
  G=24 (dB), NF=6 (dB), Loss=1 (dB)
Bi-static Parameters:
  Ptx =100 (W), Gtx=40 (dB), Grx=24 (dB)

## Slide 9: Optimistic Link Budget
Monostatic Parameters:
  RCS = -20 (dBsm), Bw = 100e3 (Hz)
  Ptx = 1 (kW), Freq=30e9 (Hz)
  G=30 (dB), NF=6 (dB), Loss=1 (dB)
Bi-static Parameters:
  Ptx =10 (kW), Gtx=40 (dB), Grx=24 (dB)
For optimistic power and gain parameters, the SNR is become positive for the given RCS and geometry under 5 km, resulting in the target being coming detectable.
Note: Generally, there is a burn through range at which a mono-static seeker outperforms the bi-static seeker. Also, note that coherently integrating 64 pulses is only applicable to the mono-static case.

## Slide 10: Challenges – Clutter, RCS
Base-band frequency
In order to solve these hardware radar problem, it is better to build a custom seeker instead of trying to repurpose a solution from a company like ImSAR
Notes: https://www.researchgate.net/figure/Ku-band-clutter-reflectivity-values-at-30-degree-grazing-angle-VV-polarization-13_tbl1_253215976
https://www.semanticscholar.org/paper/Numerical-Computation-of-the-Radar-Cross-Section-of-Kenyon-Dogaru/6c3170d1f8725bf1e552b63e0fda76527949e100
https://apps.dtic.mil/sti/pdfs/ADA622300.pdf